WINDOW FILM: CLEANING/AFTER CARE INSTRUCTIONS

INSTALLATION:

The curing period of the adhesive to the window often causes a slightly misty appearance.  This is normal and will clear in a short period of time (usually around 7 - 20 days) depending on the thickness of the film.

In very cold weather the curing process may take longer and the mistiness more pronounced.  Nevertheless the film will clear to provide perfect clarity.

To remove existing film the outer layer of film needs to be peeled away from the glazing surface. This can be done with flat sharp stripping blades or by carefully pulling the film from the top corners. Once the outer layer of film is removed the adhesive residual adhesive should be soaked with a water and detergent solution for 3-5 minutes. Once softened the same flat scrapper can be used to remove the adhesive.

Careful consideration needs to be given to retaining the adhesive and not allowing it to come into contact with carpets, soft furnishings, etc.

SECURITY FILM

Small bubbles of water (up to 2.5 cm diameter) may appear after installation.  These are simply small globules of water collecting into larger pockets.  During the curing period (up to 60 days) these will disperse and ultimately leave you with superb protection.

PLEASE under no circumstances touch the window film or attempt to “push out” any bubbles.

AFTER CARE

Do not clean the window for 28 days.  Thereafter, only use a chamois leather, soft cloth or rubber squeegee.

After the curing period, “point of sale” literature can be stuck to the film.  Please do not use stickytape because of the aggressive adhesive.  We would advise the use of Simple tape which has a low tack adhesive.  This is a white tape available from stationery stores.

When fitting credit card signs and other permanent posters, we would advise that the area is sprayed with soapy water to allow the poster to be positioned correctly and then allowed to dry out naturally.

The product after the curing period can be cleaned in the normal way using soapy water and window wipe.  We do not advise the use of window creams but a silicone spray polish can be used to enhance the appearance.

DO NOT USE BRUSHES OR ABRASIVE CLEANERS